## Slide 1
a&e REPORTING
REQUIREMENTS

## Slide 2
MLSR
Malfunction Reporting
Defect Reporting
Explosives Mishap Reporting
Class B Mishap AT-4 Discharge (example)
a&e reporting
requirements

## Slide 3
a&e reporting
requirements
Missing, Lost, Stolen, or Recovered (MLSR) Report
An MLSR must be submitted for any of the items listed below within 48 hours: (MCO 5530.14A, appendix L)
  One or more missile or rocket rounds
  One or more machine guns
  One or more automatic fire weapons
  One or more manually operated semiautomatic weapons
  Over 1,000 rounds or more of ammunition smaller than 20mm
  Individual rounds of 20mm and larger ammunition

## Slide 4
MLSR reportable quantities continued:
  Any frag, concussion, or HE grenades including artillery or ground burst sims, or any other simulator or device containing explosive material
  Demolition explosives and detonators including det cord, DETA sheet, cutters, flexible linear shape charges, blocks of explosives, other explosives, and blasting caps
a&e reporting
requirements

## Slide 5
a&e reporting
requirements
MLSRS reportable quantities continued:
  Armed or attempted armed robberies of AA&E facilities
  Forced or attempted forced entries into AA&E facilities
  Evidence of terrorist involvement in the theft of AA&E
  Incidents involving AA&E that cause significant news coverage, or appear to have the potential to cause such coverage
  Evidence of trafficking or bartering involving AA&E, illegal drugs, etc., regardless of the quantity of AA&E involved

## Slide 6
Malfunction Report
Malfunction
  The failure of an ammunition item to function as designed, intended, and expected performance when fired.
All ammunition malfunctions require reporting by the organization.
  Class A – Any Malfunction resulting in Fatality or Permanent Total Disability, or property damage is excess of 2 million dollars.
  Class B – Any Malfunction resulting in Permanent Partial Disability, or when 3 or more personnel are hospitalized for impatient care, or property damage between 500,000 and 2 million dollars
  Class C – Any Malfunction resulting in one or more days from work or property damage between 50,000 and 500,000 dollars.
  Class D – Property damage below 50,000 dollars.
a&e reporting
requirements

## Slide 7
Units experiencing a Class A, B, or C Malfunctions shall contact MARCORSYSCOM within 8 hours of malfunction by telephone.
  An initial malfunction report must be submitted within 24 hours via naval message.
  A supplemental malfunction report shall be submitted within 5 working days of the malfunction via naval message.
a&e reporting
requirements

## Slide 8
Class D Malfunctions will be reported within 96 hours of malfunction
  Conduct formal investigations involving casualties, equipment damage, and potential safety issues.
Reference: MCO 8025.1E and Class V(W) Malfunction and Defect Reporting message dtd 132004Z Apr 12.
a&e reporting
requirements

## Slide 10
Defect Reporting
Defect
  An imperfection which may prevent an item from functioning as intended or result in a malfunction.
Employment of a defective A&E item may result in casualties and or weapons damage.
When a defect is detected the following actions are required;
    Return the defective item to the ASP
    A Defect report will be submitted within 5 days of the defect being Identified.
Reference: MCO 8025.1E and Class V(W) Malfunction and Defect Reporting message dtd 132004Z Apr 12.
a&e reporting
requirements

## Slide 11
D579 - Exudate from fuze wells - 2004.
Reported by USMC at Army storage sites.
Cause is an impurity in the TNT filler in the projo.
Rounds w/ noticeable exudate should be reported, destroyed – not fired, per AIN.
a&e reporting
requirements

## Slide 12
C870 - Cracked fins - 2004. Reported by USMC during renovation at CLNC.
Cause of cracking was determined to be use of non-spec aluminum during manufacture.
Renovation to replace fins has been completed.
a&e reporting
requirements

## Slide 14
Description of the Mishap:
  Marine was on the M249 saw and was firing the weapon in short bursts. The weapon, which had previously been firing smoothly and consistently, experienced a stoppage. Marine commenced to conduct his immediate action to the stoppage, racked the weapon, and unsuccessfully attempted to resume firing. At this time he transitioned into his proper remedial action, ducking his head away from the weapon so that his helmet would offer protection. He then waited eight seconds prior to opening the feed tray cover. Upon doing so, the apex group civilian contractor, reached out to clear away the ammunition and check for any obstructions. As the civilian contractor was reaching towards the feed tray, one of the rounds exploded causing a blast injury to the civilian contractors hand, and minor burns to the Marine’s wrist and face. Both individuals were taken to the Camp Lejeune Naval Hospital, were treated, and resumed training.
a&e reporting
requirements

## Slide 15
Explosives Mishap Reporting
Establish WESS accounts using the WESS reporting link from:
  COMNAVSAFECEN homepage or http://safetycenter.navy.mil/
    via safe_wesshelp@navyil
    via siprnet to rfk_safetycenter@navy.smil.mil
    via m_nrfk_safetycenter@navy.smil.mil
  http://safetycenter.navy.mil/wess/
  ESAMS (MCIEAST)
a&e reporting
requirements

## Slide 16
Those explosives incidents that do not meet the mishap severity classification of class A, B, or C will be reported as an Explosives Event Report (EER).
Reference: MCO 5100.29B.
a&e reporting
requirements

## Slide 17
Cocking Lever was in the cocked position

## Slide 18
AT-4 impacted in the ground near the Marines feet.

## Slide 19
Class B Mishap AT-4 Discharge
Who: Two Marines
  Both Marines were with a Mar Div (FWD) on foot.
What: AT-4 discharge, blast caused loss of four fingers to left hand of 1st Marine and left tympanic membrane rupture, disorientation, and confusion to the 2nd Marine (non-permanent injury)
When: 2010
Where: FOB
a&e reporting
requirements

## Slide 20
During August an Infantry Company Arrived at the FOB
The Company left all equipment they could not carry while dismounted at a Company Resupply Point under a solar shade on the FOB.
They departed the FOB to conduct dismounted combat operations in the green zone. Two Marines were left with the Remain Behind Element to guard the Equipment.
The 1st Marine was handling an AT-4 when it discharged, impacting the ground and sustained the loss of four fingers on his left hand due to the blast.
The 2nd Marine sustained a left tympanic membrane rupture, disorientation, and confusion due to being in the vicinity of the blast.
a&e reporting
requirements

## Slide 21
Both Marines were medically evacuated to a Medical Facility.
Neither Marine was wearing PPE, as it is not required while on the FOB.
1sMarine is currently located at a Navy Medical Center.
2d Marine is in outpatient care at the Wounded Warrior Battalion (WWB) being treated for headaches and nausea. The Tympanic Membrane Rupture is expected to heal.
a&e reporting
requirements

## Slide 22
Ammunition Holding Areas (AHA) have been established at all Forward Operating Bases.
The Battalion Commander has directed the inspection of all AT-4 Rockets. All grade 3 rockets are to be turned in.
The Battalion Ammunition Technicians are circulating the battlefield to ensure compliance of all AHA’s and to collect all grade 3 munitions.
The Battalion Commander has directed reset training on the weapons handling/safety for all hands.
A Command Investigation was conducted
a&e reporting
requirements

## Slide 23
155mm In Bore Det at Ft. Bragg
Fuze functioned prematurely

## Slide 24
2 Corpsman and 8 Marines injured No Corpsman to administer 1st Aid

## Slide 25: Questions?