## Slide 1: HAZARD CLASS/DIVISION (HC/D), FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 2
Overview
Hazard Class/Divisions
Fire Hazard Symbols/Transportation Placards
Compatibility Groups (storage and transportation)
Security Risk Categories
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS
Notes: Move SRC to the end of the this class.

## Slide 3
Hazard Class
There are a total of nine different hazard classes.
Each hazard class is based on chemical and physical characteristics of the material and its reaction under various conditions.
  Hazard Class 1 – Explosives
  Hazard Class 6 – Toxic and infectious substances
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 4
Hazard Class/Division
Hazard Class 1 is composed of 6 divisions:
  Division 1 – Mass Explosion
  Division 2 – Fragment Producing
  Division 3 – Mass Fire
  Division 4 – Moderate Fire
  Division 5 – Very Insensitive
  Division 6 – Extremely Insensitive
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 5
Symbols/Placards
Fire Symbol 1 / Transportation Placard 1.1
  Do not attempt to fight fire unless a rescue attempt is being made
  Withdrawal distance is:
    2,500 ft for ≤15K NEW
    4,000 ft for >15K NEW
    D=105w1/3 ft >50K NEW (1/3 is cube root)
  Examples - Hand Grenades, general purpose bombs, and 40 mm HEDP
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 6
Fire Symbol 2 / Transportation Placard 1.2
  Do not attempt to fight fire unless a rescue attempt is being made
  Attempt to extinguish the fire if it is in an early stage. Prevent spreading of the fire if possible.
  Withdrawal distance is 2,500 ft
  Examples – HE mortars, tank rounds
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 7
Fire Symbol 3 / Transportation Placard 1.3
  These fires may be fought if explosives are not directly involved.
  Withdrawal distance is 600 ft
  Examples – 155mm Illum rds, Flares, and signal illums.
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 8
Fire Symbol 4 / Transportation Placard 1.4
  Do not attempt to fight fire unless a rescue attempt is being made
  Fight these Fires
  Withdrawal distance is 300 ft
  Examples - 7.62mm, 5.56mm, 45 cal, and 9mm ammunition
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 9
Chemical Hazard Symbols
Set 1
  Round Sign with red border, blue background and a red figure in protective clothing.
  Indicates the presence of a highly toxic chemical agent.
  Examples - Nerve and Blister Agents
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 10
NAVSEA OP5 VOL. REV 7
Set 2
  Round Sign with a yellow border, blue background with a yellow figure in protective clothing
  Indicates the presence of harassing agents.
  Response will be from an upwind direction in protective clothing.
  Examples - Choking gases, vomiting agents, and screening smokes.
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 11
NAVSEA OP5 VOL. REV 7
Set 3
  Round Sign with white border, blue background, white figure in protective clothing.
  Indicates the presence of white phosphorus
  Response approach if smoke is present will be in full protective clothing
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 12
NAVSEA OP5 VOL. REV 7
Apply No Water!
  If water is added, it could intensify the flames.
  Munitions burn with extremely high temperatures and are difficult to extinguish.
  Do not look directly at material since eye damage may result.
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 13
NAVSEA OP5 VOL. REV 7
Wear Breathing Apparatus
  This indicates the presence of toxic smokes.
  Protective mask is required for fighting these fires.
  The gas mask that you are issued is not the mask you want to use.
  Do not use water.
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 14
Compatibility Groups
Based on the type/degree of risk the A&E items present in storage and transportation.
A&E is assigned to a storage compatibility group (SCG) when they can be stored / transported together without increasing significantly either the probability of an accident or for a given quantity, the magnitude of the effects from such an accident.
A&E is further categorized in to 13 compatibility groups.
  A, B, C, D, E, F, G, H, J, K, L, N, S
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 15
A: Bulk initiating explosives that have the necessary sensitivity to heat, friction or percussion (RDX/PETN)
B: Detonators and similar initiating devices not containing two or more independent safety features (Blasting Caps)
C: Bulk propellants, propelling charges & devices containing propellant with or without their own means of ignition.
D: Black powder, HE & ammo containing HE without its own means of initiation & w/o propelling charge (Demo)
E: HE & ammo containing HE without its own means of initiation & w/o propelling charge HE (Arty/Rockets)
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 16
F: Ammo Containing HE with its own means of initiation & with Propelling Charge (Frag Grenades)
G: Fireworks, illuminating, incendiary & smoke (Pyro & Small Arms)
H: Ammo containing both explosives & WP
S: Ammo presenting no significant hazard (Small Arms)
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 17
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 18
Notes
The marking “X” at an intersection of the above chart indicates that these groups may be combined in storage. Otherwise, mixing is either prohibited or restricted per note 2 below.
The marking “Z” at an intersection of the above chart indicates that, when warranted by operational considerations or magazine non-availability, and when safety is not sacrificed, logical mixed storage of some items of different groups may be authorized by NOSSA upon written request. Mixing of limited quantities of some groups, as authorized by note 5 below, does not require a written request. Authorization is not to be considered a waiver. Combinations that violate the principles of paragraph 3-9 require justification by waiver or
exemption. Examples of acceptable combinations of class 1 are:
  Division 1, group A initiating explosives with division 1, group B fuzes not containing two or more independent safety features.
  Division 3, group C bulk propellants or bagged propelling charges with division 3, group G pyrotechnics without their own means of initiation.
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 19
Equal numbers of separately packaged components of complete rounds of any single type of ammunition may be stored together. When so stored, compatibility is that of the assembled round; i.e., WP filler in group H, HE filler in groups D, E, or F, as appropriate.
Ammunition designated “practice” by NSN and nomenclature may be stored with the fully loaded ammunition it simulates.
Mixing of compatibility groups (except items in groups A, K, and L) is authorized when the total quantity does not exceed 1,000 pounds NEW. Mixed storage that exceeds 1,000 pounds NEW must be approved by NOSSA.
Mixing in storage of hazard Class 1 ammunition or ammunition components with hazard Class 2 through 9 ammunition or ammunition components, or with non-regulated items assigned a compatibility group, is authorized, provided storage is in accordance with the compatibility group assigned.
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 20
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 21
For motor vehicles the letter “X” in the table indicates that explosives of different compatibility groups may not be carried on the same transport vehicle. For railcars the letter “X” indicates that explosives of different compatibility groups may not be carried on the same railcar unless packed in separate freight containers (e.g. two or more freight containers mounted upon the same railcar).
Means explosives from compatibility group L may only be carried on the same motor vehicle or railcar with an identical explosive.
Means any combination of explosives from compatibility group C, D, or E is assigned to compatibility group E.
Means any combination of explosives from compatibility group C, D, or E with those in compatibility group N is assigned to compatibility group D.
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 22
Means detonators and detonating primers, Division 1.4S (Class C explosives), may not be loaded in the same railcar with Division 1.1 and 1.2 (Class A explosive) materials as described in 49 CFR 174.81 (g)(3)(iv). Also, see 49 CFR 177.835 (g) for restrictions of detonator assemblies, boosters with detonators, and detonators on public highway.
Means Division 1.4S fireworks may not be loaded in the same motor vehicle or rail car with Division 1.1 or 1.2 (Class A explosive) materials.
Means explosive articles in compatibility group G, other than fireworks and those requiring special stowage, may be stowed with articles of compatibility groups C, D and E, provided no explosive substances are carried in the same vehicle.
HC/D, FIRE SYMBOLS, AND COMPATIBILITY GROUPS

## Slide 23: Questions